NOT Inspections Module 1 Printout

## 1.3 Learning Goals

Notes:

Welcome to this course on Notice of Termination, or NOT, inspections. This course is broken up into four modules. In Module 1, we will discuss some guidelines for NOT inspections such as recommended times to conduct the inspection, who to invite on the inspection, common PCSM BMP failures, and permit termination.

## 1.4 Schedule Inspection During or Just After Runoff Event

Notes:

If possible, it is best for inspection personnel to schedule final inspections during or just after a recent runoff event in order to determine if BMPs appear to be functioning properly. If the BMP is holding water after a recent runoff event, it can be more easily determined if leakage within the overflow structures is occurring. It can also help to determine if proper drainage to the BMPs has been achieved or if runoff is bypassing the BMP designed to receive and treat the runoff.

## 1.5 Invite the Developer or Permittee

Notes:

It is recommended that inspection personnel invite the developer, or NPDES permittee, to the notice of termination inspection. This can help avoid any miscommunication in the associated inspection report. It can also help the permittee learn about what BMPs may need to be repaired, what was not constructed per the project plan requirements and what must be done to repair any BMP failures.

## 1.6 Common PCSM BMP Failures

Notes:

Site inspections have shown that a very high rate of infiltration BMP failures are common.  Many of these failures are associated with issues related to poor design specifications such as a failure to limit the amount of clay in the soil mixture, lack of requirement to ensure watertight joints and pipe penetrations in overflow devices or lack of direction to provide immediate stabilization of the BMP soil surface after construction.  Almost all failing infiltration BMPs have some degree of construction error such as failure to use the specified soil mixture, compaction of the BMP bottom, failure to provide watertight joints and pipe penetrations, failure to stabilize the BMP soils and associated drainage areas or a combination of several factors.  Conservation districts who have an Engineering Delegation with DEP can help to resolve design issues during the technical Post Construction Stormwater Management plan review.

## 1.7 Infiltration BMPs

Notes:

Infiltration BMPs must be constructed per project requirements and properly functioning as credited prior to NPDES Permit termination. Leaking overflow piping is very common and is considered a failure since the captured runoff is being discharged untreated instead of infiltrating into the soil where associated pollutants can be removed and the groundwater replenished.

## 1.8 Leaks and Open Valves

Notes:

Inspection personnel should diligently observe outlet and overflow structures for signs of leakage or valves that have been left open.  In most cases, valves are specified only to be opened if necessary to drain BMPs in the event of failure and subsequent required maintenance.  Leaking structures and valves left open are very common and generally result in a reduction or loss of adequate water quality treatment as required by the NPDES permit.  It is common that valves in underdrain piping are left open by construction personnel so that the BMPs drain, leading to the appearance that an infiltration BMP is infiltrating correctly but is actually draining out the outlet piping, leading to discharge of runoff water that was likely credited for infiltration volume credits.  Some BMPs have under-drains specified so it is important to understand if any associated volume or infiltration credits have been voided by the use of under-drains.

## 1.9 Infiltration BMPs Which Hold Runoff In Excess of 72 Hours

Notes:

Infiltration BMPs that are holding runoff at the surface in excess of 72 hours or are observed to be overflowing during small runoff events are likely failing to infiltrate as designed and credited.  Infiltration BMPs that hold water in excess of the calculated drawdown period can be considered a reduction or failure of the BMP.  This type of failure is fairly common, especially where soils high in clay content are predominant and where compaction or damage from the impacts of falling raindrops on un-stabilized soils had occurred during construction of the BMP.

## 1.10 Nitrate is pollutant of concern!

Notes:

Worksheet 10 from the 2006 post construction stormwater BMP manual provides BMPs that can be used to show water quality compliance for nitrate. The intent of these BMPs is to provide water quality results across the site, not just small areas of an overall large permitted site. These BMPs should be clearly shown on the post construction stormwater management plan.

Street sweeping is one of the BMPs that can be used to show water quality compliance for nitrate but is commonly omitted from actual site operations.

Inspection personnel should look for evidence of street sweeping such as sweeping lines or marks left on asphalt areas. In the absence of clear indication that street sweeping is being conducted, inspection personnel should ask the permittee for proof that street sweeping is being conducted at the proper frequency. It is also important that the proper street sweeping equipment is being used. Many sweeper trucks sweep accumulated pollutants to the side where subsequent rain events will wash them into the storm sewer and possibly to receiving surface waters. Vacuum assisted sweeper trucks can remove the pollutants but the captured sweepings must be disposed of properly. Sweeping and disposal techniques as well as sweeping frequencies should be clearly specified in the operations and maintenance section of the project plans.

## 1.11 E&S BMPs removed and Site Stabilized?

Notes:

Have the E&S BMPs been removed and the site permanently stabilized?

All temporary sediment control BMPs must be removed prior to permit termination.  The site must have permanent stabilization as per the project specifications. The inlet protection in this photo has been there long enough for wetland vegetation to start growing in the captured sediments.

## 1.12 What if PCSM BMPs Aren't Functioning?

Notes:

What happens if the PCSM BMPs are not properly functioning?

Per the NPDES Permit Management Requirements, section H:  Reduction, Loss or Failure of BMP: “Upon reduction, loss, or failure of any BMP, the permittee and co-permittee shall take immediate action to restore, repair, or replace the BMP or provide an alternative method of treatment.”  This section of the NPDES permit requires the permittee or co-permittee to mitigate and repair any reduction or loss of treatment or other failures of BMPs immediately upon discovering the issue.

Inspection personnel should document all reduction, loss or failure of BMPs as a “failure to implement effective PCSM BMPs” and “sediment or other pollutant was discharged into waters of the Commonwealth”.

## 1.13 NPDES Permit Termination

Notes:

If the NPDES Permit is not terminated as required, the developer, or permittee, and any co-permittees remain responsible for the long-term operations and maintenance requirements of the BMPs in accordance with Chapter 102.8(m)(5).

## 1.14 Summary

Notes:

This concludes Module 1. To review, it is recommended to conduct inspections during or shortly after a runoff event. It is recommended to invite the developer and permittee along on the inspection. Common PCSM BMP failures include leaks, lack of infiltration, and lack of stabilization. If the permit is not terminated, permittees are responsible for the long-term operation and maintenance requirements of BMPs.

Next, there is a knowledge check.