## Slide 1: Manure management plan summary – pasture rates
Completing a Manure Management Plan Workshop
v.12.2012
Notes: This is an optional module that illustrates how to determine a mechanical manure application rate on pastures. It is to be used in conjunction with the factsheets for horses, dairy, beef, sheep and goats.

## Slide 2: Mechanical Application on Pastures
Determining Mechanical Manure Application Rates Worksheets
  For pastures where there will be grazing AND mechanical manure application
Five worksheets currently available
  Beef
  Dairy
  Goat
  Horse
  Sheep

## Slide 3
Each packet includes:
  Worksheet
  Instructions
  Example

## Slide 5: Steps To Determine Maximum Rate
Determine if the rate will be based on nitrogen or phosphorus
  Nitrogen
    Soil tests <200 ppm P
  Phosphorus
    Soil tests > 200 ppm P
    No soil tests
Select the Manure Application Rate Table
  Manure type
    Animal type and solid manure
  Rate basis
    Nitrogen or Crop Phosphorus Removal
Select the “Grass Hay” crop group
  Select the lowest yield for Grass Hay across the top

## Slide 6: Steps To Determine Maximum Rate
Under “Manure Application Method” find the application method that corresponds to when the manure will be applied
  Spring and summer applications
    Choose “Spring No Incorporation”
  Fall applications
    Choose “Fall”
  Winter applications
    Choose “Winter With Cover Crop”
Note where the application method and manure in tons/acre intersect
  This is the MAXIMUM amount of manure that can be applied per acre to the pasture

## Slide 7: Horse Pasture Example
3 acre pasture
No soil test
Manure applied spring and fall
3 light horses
  20 days: <8 hours
  100 days: 12 hours
  200 days: >16 hours
Total Maximum Manure – 10 T/A

## Slide 8
 | Tons | X | Days on Pasture | X | Number of Animals | = | Tons of Manure from Grazing
LIGHT HORSES |  |  |  |  |  |  | 
Less than 8 Hours | .010 | X |  | X |  | = | 
8-16 Hours | .020 | X |  | X |  | = | 
Over 16 Hours | .030 | X |  | X |  | = | 
Total Manure Applied by Grazing Animals (ton) Add the amounts calculated above |  |  |  |  |  | = | 
Acres in the Pasture |  |  |  |  |  |  | 
Manure Applied per Acre by Grazing Animals (ton/A Divide the total manure applied by grazing animals by the acres in the pasture |  |  |  |  |  |  | 
Maximum Allowable Rate (ton/A) From MMM Rates Table for horse manure |  |  |  |  |  | = | 10
Allowable Mechanical Manure Application Rate (ton/A) Difference between the manure applied by grazing animals and the maximum allowable rate |  |  |  |  |  | = | 

## Slide 9: Steps To Determine Grazing Manure
Use the “Calculation Worksheet”
  Number of animals in each group
  Days out of the year each group is grazed
    Estimate to within + 10 days
    Does not have to equal 365 days if there are days when animals are not on the pasture
    If pastures are grazed differently calculate for each pasture
  Multiply the following to determine the tons/acre from grazing
    Worksheet “Tons” factor
    Days on pasture
    Number of animals
  Add each line to determine “Total Manure Applied by Grazing Animals”

## Slide 10
 | Tons | X | Days on Pasture | X | Number of Animals | = | Tons of Manure from Grazing
LIGHT HORSES |  |  |  |  |  |  | 
Less than 8 Hours | .010 | X | 20 | X | 3 | = | .6
8-16 Hours | .020 | X | 100 | X | 3 | = | 6.0
Over 16 Hours | .030 | X | 200 | X | 3 | = | 18.0
Total Manure Applied by Grazing Animals (ton) Add the amounts calculated above |  |  |  |  |  | = | 24.6
Acres in the Pasture |  |  |  |  |  |  | 
Manure Applied per Acre by Grazing Animals (ton/A Divide the total manure applied by grazing animals by the acres in the pasture |  |  |  |  |  |  | 
Maximum Allowable Rate (ton/A) From MMM Rates Table for horse manure |  |  |  |  |  | = | 10
Allowable Mechanical Manure Application Rate (ton/A) Difference between the manure applied by grazing animals and the maximum allowable rate |  |  |  |  |  | = | 

## Slide 11: Steps To Determine Grazing Manure
Determine the number of acres in the pasture
Divide the total manure applied by the grazing animals by the acres
  Amount of manure per acre applied by the grazing animals

## Slide 12
 | Tons | X | Days on Pasture | X | Number of Animals | = | Tons of Manure from Grazing
LIGHT HORSES |  |  |  |  |  |  | 
Less than 8 Hours | .010 | X | 20 | X | 3 | = | .6
8-16 Hours | .020 | X | 100 | X | 3 | = | 6.0
Over 16 Hours | .030 | X | 200 | X | 3 | = | 18.0
Total Manure Applied by Grazing Animals (ton) Add the amounts calculated above |  |  |  |  |  | = | 24.6
Acres in the Pasture |  |  |  |  |  |  | 3
Manure Applied per Acre by Grazing Animals (ton/A Divide the total manure applied by grazing animals by the acres in the pasture |  |  |  |  |  |  | 8.2
Maximum Allowable Rate (ton/A) From MMM Rates Table for horse manure |  |  |  |  |  | = | 10
Allowable Mechanical Manure Application Rate (ton/A) Difference between the manure applied by grazing animals and the maximum allowable rate |  |  |  |  |  | = | 

## Slide 13: Determine Mechanical Manure Rate
Subtract the manure applied per acre from the maximum allowable rate

## Slide 14
 | Tons | X | Days on Pasture | X | Number of Animals | = | Tons of Manure from Grazing
LIGHT HORSES |  |  |  |  |  |  | 
Less than 8 Hours | .010 | X | 20 | X | 3 | = | .6
8-16 Hours | .020 | X | 100 | X | 3 | = | 6.0
Over 16 Hours | .030 | X | 200 | X | 3 | = | 18.0
Total Manure Applied by Grazing Animals (ton) Add the amounts calculated above |  |  |  |  |  | = | 24.6
Acres in the Pasture |  |  |  |  |  |  | 3
Manure Applied per Acre by Grazing Animals (ton/A Divide the total manure applied by grazing animals by the acres in the pasture |  |  |  |  |  |  | 8.2
Maximum Allowable Rate (ton/A) From MMM Rates Table for horse manure |  |  |  |  |  | = | 10
Allowable Mechanical Manure Application Rate (ton/A) Difference between the manure applied by grazing animals and the maximum allowable rate |  |  |  |  |  | = | 1.8
Rate of mechanically applied manure cannot be greater than 1.8 tons/acre.

## Slide 15: Manure Management Plan Summary
Crop Group and Yield (a) | Manure Group (b) | Application Season (c ) | Planned Application Rate from C, NBS, PI * (d) | Incorporation Timing (e) | Commercial Fertilizer Application Rate (f) | Fields where this crop group can be used (g)
Pasture (3 T/A) | Solid Horse | Spring, Fall | 1.5 T/A ‘C’ | No Incorpor. | NA | Pastures 1, 2, 3